## Slide 1
Learning to Dispatch for Job Shop Scheduling via Deep Reinforcement Learning
Cong Zhang1, Wen Song2, Zhiguang Cao3, Jie Zhang1, Puay Siew Tan4, and Chi Xu4
1Nanyang Technological University
2Institute of Marine Science and Technology, Shandong University, China
3National University of Singapore
4Singapore Institute of Manufacturing Technology, A*STAR

## Slide 2
CONTENTS
Background
Learning to dispatch (L2D)
Experiment
Conclusion

## Slide 3
CONTENTS
Background
Learning to dispatch (L2D)
Experiment
Conclusion

## Slide 4
1
Job-Shop Scheduling Problem & Disjunctive Graphs
Background
Job-Shop Scheduling Problem (JSSP) is a well-known Combinatorial Optimization Problem (COP) that is NP-hard to solve.
, , , s.t holds
Disjunctive Graph (DG) is a concise way of representing combinatorial properties of JSSP and schedules.
(a) JSSP instance
(b) Complete Solution

## Slide 5
1
Motivation
Background
Priority Dispatching Rule (PDR) is a class of heuristics that is widely used to solve real-world JSSP:
  Based on some calculated priority indices, it schedules, within the current waiting list, the job with highest index.
However, the design of effective PDRs is a tedious task:
  Requiring a myriad of specialized knowledge;
  Delicate and limited performance for different JSSPs;
Q: How to search the PDR space automatically to find PDR that has robust generalization and strong performance?
Notes: asdasda

## Slide 6
1
Challenges
L2D
Challenges
  Due to strong NP-hardness, how to search the PDR space efficiently and effectively in an end-to-end & un-supervised manner?
  Can learning be size-agnostic so that learned PDR would generalize to un-seen large-scale instances?
+
Graph Neural Networks
Learning to Dispatch

## Slide 7
CONTENTS
Background
Learning to dispatch (L2D)
Experiment
Conclusion

## Slide 8
2
Markov Decision Process Formulation
L2D
State: disjunctive graph presenting current solution; initial state is the DG of original JSSP; terminal state is a complete solution;
Action: is an eligible operation at time ;
Reward: where is the lower bound of makespan ;

## Slide 9
2
Parameterizing the Policy
L2D
We use GIN as state embedding network as it is one of the strongest GNN for homogeneous graphs with proved discriminative power.
For each layer :
Proximal Policy Optimization (PPO) as optimizer

## Slide 10
2
Learning Algorithm
L2D
We choose Proximal Policy Optimization as optimizer of our agent:
Optimizing our agent over four independent JSSP instances per iteration;

## Slide 11
CONTENTS
Background
Learning to dispatch (L2D)
Experiment
Conclusion

## Slide 12
3
Datasets & Baselines
Experiment
Datasets: (instances underscored are used in generalization test)
  Synthetic dataset: , , , , , , .
  Open Benchmark:
    Taillard’s instances: , , , , , , , .
    DMU instances: , , , , , , ,
Baselines:
  Four existing strongest PDRs: SPT, MWKR, FDD/MWKR, MOPNR

## Slide 13
3
Results on Synthetic Dataset
Experiment

## Slide 14
3
Results on Open Benchmarks - Taillard
Experiment

## Slide 15
3
Results on Open Benchmarks - DMU
Experiment

## Slide 16
CONTENTS
Background
Learning to dispatch (L2D)
Experiment
Conclusion

## Slide 17
4
Conclusions
It is the first attempt to directly learn strong PDRs based on disjunctive graph representation.
Learned PDR has robust generalization.